## Slide 1
Bridging Natural Language to Verified Implementation
A Neuro-Symbolic High-Assurance MBSE Pipeline in SysML v2
IEEE/AIAA DASC 2026
Amer Tahat, David Hardin, Isaac Amundson, Junaid Babar, Timothy A. Barclay, Janet Liu, Karl Hoech, and Darren Cofer
Collins Aerospace, an RTX Business
Distribution Statement A. Approved for public distribution; distribution unlimited.
This work was funded by DARPA contract FA8750-24-9-1000. The views expressed are those of the authors.
1
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:35
Presenter focus: introduce the pipeline, industrial constraints, and the role of Meta-Rules and formal verification.
What I would say:
Good morning. In this talk, we present an agentic, neuro-symbolic MBSE pipeline that turns English requirements and SysML v2 architecture context into formal GUMBO contracts, HAMR-generated implementation artifacts, and Logika-verified evidence.
The challenge is doing this under practical industrial constraints: restricted fine-tuning, proprietary data, and limited context, time, tokens, and human review. Our approach captures successful adaptation as persistent Meta-Rules, while formal verification remains the acceptance gate. I will briefly cover the problem, our method, and the Isolette results.
Presenter suggestion: deliver this in about 35-40 seconds; save technical definitions for the following slides.
Claim guardrail: the quantitative evidence is scoped to the defined Isolette/HAMR evaluation.
Transition: Let me begin with why plausible GenAI output is not enough for high-assurance engineering.
<number>

## Slide 2
Intro: Why GenAI needs proof
Plausible artifacts are useful drafts; certification-facing workflows require traceability and machine-checkable acceptance.
1
What GenAI does well
Reads natural-language requirements
Drafts model- and code-like artifacts quickly
Repairs from examples and feedback
2
What assurance requires
Traceability from requirement to implementation
Repeatable evidence - not persuasive prose
Machine-checkable correctness across layers
3
Research question
Can an agent produce a verifier-accepted implementation from English requirements
while bounded by time, tokens, repair cycles, and human review?
Engineering objective: produce a verifier-accepted artifact before the budget is exhausted.
Source: Tahat et al., DASC 2026, Abstract and Introduction.
2
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:55
Presenter focus: define the problem for non-specialists.
What I would say:
GenAI is useful for drafting, but in avionics the hard problem is not a plausible artifact. The hard problem is producing accepted evidence: traceable, repeatable, machine-checkable evidence within a budget. Our research question is whether an agent can start from English requirements and end with verifier-accepted artifacts before time, tokens, repair cycles, and human review are exhausted.
Transition: The next slide places this inside DARPA PROVERS and the INSPECTA toolchain.
<number>

## Slide 3
Intro: DARPA PROVERS, INSPECTA, and SCP
PROVERS supplies the mission; INSPECTA supplies the proof stack; SCP supplies the natural-language adaptation layer.
1
2
3
4
Sources: DARPA PROVERS / INSPECTA background from HCSS 2026 material; SCP framing from Tahat et al., DASC 2026.
3
DARPA PROVERS
Automated, scalable formal-methods tools integrated into traditional engineering pipelines.
Mission
INSPECTA
Collins-led proof-engineering toolchain: SysML v2, GUMBO, HAMR, Logika, and proof evidence.
Formal backbone
SCP Copilot
Low-entry natural-language layer that generates, specializes, repairs, and records verified traces.
Agent layer
GenAI accelerates engineering; formal tools decide what is accepted.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:05
Presenter focus: explain the program context in plain language.
What I would say:
PROVERS is the broader DARPA motivation: integrate scalable formal methods into development pipelines so product engineers can incrementally build high-assurance systems. INSPECTA is the proof-engineering backbone: SysML v2, GUMBO, HAMR, Logika, and proof artifacts. SCP Copilot is our agentic layer. It helps generate, specialize, and repair formal artifacts, but the formal tools decide primarily what is accepted after human final approval.
Transition: Now I will define Spec-Code-Proof as a layered assurance MBSE agentic pipeline.
<number>

## Slide 4
Intro: What Spec-Code-Proof means
A layered assurance object—not a single text-to-code prompt.
Generator
proposes a candidate
Verifier
checks all encoded cases
PASS
proof artifact emitted
FAIL
diagnostic or counterexample returns to repair
The LLM proposes; the checker decides.
Layered assurance object
English requirements
intent + traceability
SysML v2 architecture
components, threads, ports, connections
GUMBO contracts
state, assumptions, guarantees, compute cases
HAMR generation
memory-safe infrastructure + proof obligations
Logika / SMT proof
integration- and code-level discharge
A contract that parses but attaches to the wrong thread is still a failure. A proof must survive the whole path.
Source: Tahat et al., DASC 2026, Sec. II-A and Fig. 1; Hatcliff et al., HAMR / GUMBO background.
4
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:05
Presenter focus: make the pipeline understandable before technical details.
What I would say:
Spec-Code-Proof is not a single text-to-code prompt. English requirements and architecture context become SysML v2 structure. Behavioral intent is encoded in GUMBO contracts. HAMR generates implementation infrastructure, and Logika/SMT discharges proof obligations. Proof here means external tool evidence that properties survive across layers—not an LLM explanation only.
Transition: With that background, here are the paper contributions.
<number>

## Slide 5
Contributions: Three claims to judge
Pipeline, adaptation algorithm, and system-level evidence.
1
Trustworthy English-to-implementation pipeline
A multi-agentic pipeline generate-verify-repair loop integrated with INSPECTA: SysML v2 + GUMBO + HAMR + Logika
2
Supervised Meta-Rule self-adaptation
Successful in-context behavior becomes persistent, compact human-reviewable rule memory, screened semantically and retained only after verification within budget constrains.
3
System-level Isolette / HAMR evaluation
A realistic multi-subsystem benchmark spanning requirements, formal contracts, generated Slang/Scala obligations, and proof discharge.
Continuity: DASC 2025 established the INSPECTA SysML v2 → memory-safe code/proof path. New here: lNSPECTA SCP Copilot :low-entry English formalization + persistent verifier-gated specialization.
Sources: Tahat et al., DASC 2026, Introduction - main contributions; Hardin et al., DASC 2025,
5
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:55
Presenter focus: state the award-level intellectual nugget.
What I would say:
The paper makes three claims. First, it contributes a trustworthy English-to-implementation agentic pipeline integrated with INSPECTA. Second, it contributes supervised Meta-Rule self-adaptation: successful in-context behavior becomes persistent rule memory, but it is retained only after semantic screening, verification, and human approval. Third, it evaluates the idea on the system-level Isolette/HAMR benchmark.
Transition: The next slide explains why adding long context alone was not enough.
<number>

## Slide 6
Motivation: More context is not specialization
Repeatedly replaying requirements, models, generated code, logs, and counterexamples eventually becomes the bottleneck.
Conceptual - not an empirical fit
Attaching more files helps at first; after saturation, useful signal is diluted.
Transient ICL
Useful behavior disappears when the context resets, encouraging repeated long prompts.
Restricted fine-tuning
Domain data may be proprietary; frontier-model training authorization and checkpoint governance may be unavailable.
Niche toolchain semantics
GUMBO state, attachment, naming, generated obligations, and repair cues are sparsely represented in pretraining.
Needed: compact, governed specialization knowledge that persists across runs.
Source: Achille & Soatto (2026); conceptual scale curve.
6
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:00
Presenter focus: explain the scale diagram and why persistent abstraction is needed.
What I would say:
The conceptual curve shows the basic pressure. As inference-time context and budget increase, performance initially improves: the model gains useful task information and reward rises. Eventually, the reward curve saturates, while the learned-information curve peaks and then declines.
In our layered MBSE workflow, this motivates preserving the recurring engineering abstraction instead of replaying all requirements, models, generated code, logs, and counterexamples. EXTRACTRULE captures the reusable decision; APPLYRULE loads only what the current task needs within the available time and token budget.
Presenter suggestion: trace the rise, the saturation point, and then the decline in learned information.
Claim guardrail: the curve is a conceptual illustration, not an empirical Isolette fit or a universal saturation law.
Transition: The next slide shows how reusable structure prunes failed branches before they multiply.
<number>

## Slide 7
Motivation: Toolchain gates stop branch explosion
Early corrections prevent errors from multiplying into models, code, proof obligations, and replayed context.
1
Before: late checking
Free-form tree reasoning
2
After: toolchain-guided correction
Meta-Rules + gates
Requirement
Formalization
Placement / names
Code + proof
Natural-language requirement
unsupported @pre
explicit state?
implicit memory
3
6
candidate attachment, naming, and type choices
12
generated artifacts • proof obligations • logs
Late proof failure reveals an upstream mistake
GLOBAL REPLAY OF THE STACK
1 → 3 → 6 → 12
illustrative counts
Natural-language requirement
Rule-selected contract (explicit state)
Verified placement (owning thread)
Generated obligations (HAMR / Slang)
Verified artifact
Meta-Rule
unsupported @pre
×
Gate 1: parser + semantics
wrong thread / name
×
Gate 2: structure + placement
proof mismatch
×
Gate 3: Logika counterexample
Local diagnostic → smallest safe repair
Only one branch reaches expensive proof; failures stop locally.
Toolchain value: turn late, global failure into early, local correction—before artifacts and context multiply.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Sources: Tahat et al., DASC 2026; Achille & Soatto, 2026. Branch counts are illustrative; 18x throughput is measured later.
7
Notes: Timing: 1:05
Presenter focus: illustrate the algorithmic value of the INSPECTA/HAMR toolchain as early branch correction.
What I would say:
This slide is illustrative, but it captures why the toolchain matters. Without reusable rules and early checks, one requirement can expand into many candidate formalizations, model placements, generated artifacts, proof obligations, logs, and counterexamples before we know which branch is viable. With SCP/INSPECTA, Meta-Rules select a plausible formalization first; parser, structural, HAMR, and Logika gates reject bad branches early; and repair is localized to the smallest failing fragment. The measured consequence appears later in the results: an 18x adjusted throughput gain on the defined Isolette/HAMR scope.
Presenter suggestion: state clearly that the tree counts are illustrative, not measured node counts. The measured result is the throughput and cost change shown in the results section.
Claim guardrail: this illustrates search-pruning pressure in a layered verifier workflow; it is not a proof of a universal complexity law.
Transition: Next, I will connect this practical search reduction to related ideas about compact abstraction and reusable reasoning.
<number>

## Slide 8
Foundations: Compact abstraction is plausible
Related work motivates the design; SCP keeps the mechanism external, governed, and verifier-gated.
1
Contextual adaptation
Contextual adaptation: systems should explain and adapt to changing context, not only apply fixed rules or correlations.
Launchbury, DARPA TV, 2017
2
In-context learning
Transformers can implement learning-like updates during the forward pass without explicit deployed-weight changes.
von Oswald et al., ICML 2023
3
Task-solving transfer
Past data is valuable when it captures algorithmic structure that reduces the time needed to solve a new verified task.
Achille & Soatto, Entropy 2026
4
Selective workspace
Flexible reasoning appears to rely on a small,
privileged set of verbalizable representations amid much larger automatic processing.
Gurnee et al., Anthropic, 2026
SCP hypothesis: compact abstractions preserve useful experience, reduce repeated context, and transfer across related subsystems - enabling scoped specialization under memory and fine-tuning limits.
Sources: DARPA TV “A DARPA Perspective on AI” (2017); von Oswald et al. (2023); Achille & Soatto (2026); Gurnee et al. (2026).
8
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:55
Presenter focus: connect the related foundations to SCP's narrower engineering hypothesis.
What I would say:
These ideas help explain why compact abstraction is plausible. DARPA anticipated contextual adaptation. In-context learning shows that models can adapt during inference, but the behavior disappears when context resets. Task-solving research emphasizes reusable algorithmic structure, while Anthropic's selective-workspace result provides a useful analogy - not a mechanistic equivalence.
Our narrower hypothesis is to externalize useful abstractions into governed Meta-Rules, reuse them across related subsystems, and let formal tools accept or reject each application. This enables affordable, scoped specialization under memory, token, and fine-tuning constraints.
Claim guardrail: these are motivating foundations and analogies; accepted quantitative evidence remains scoped to the Isolette/HAMR evaluation.
Transition: With that foundation, I will now show what a machine-checkable GUMBO contract looks like.
<number>

## Slide 9
Method: GUMBO contracts make behavior checkable
Behavioral intent becomes machine-checkable assume/guarantee structure.
Natural-language intent
If the regulator is in NORMAL mode and temperature is below the lower desired bound, heat control shall be On.
When a hysteresis band requires “no change,” preserve the previous command.
Requirement words such as “hold previous” imply memory.
Illustrative GUMBO contract
language "GUMBO" /* {
state lastCmd: On_Off;
initialize
guarantee initLastCmd: lastCmd == Off;
compute
assume lowerLEUpper: lower <= upper;
guarantee lastCmdTracksOutput:
lastCmd == heat_control;
compute_cases
case REQ_1:
assume mode == INIT;
guarantee heat_control == Off;
case REQ_2:
assume mode == NORMAL && temp < lower;
guarantee heat_control == On;
} */
What the checker sees
state: memory is explicit
initialize: initial value is constrained
assume: input/environment constraints
guarantee: required behavior
compute cases: conditional traceability
placement: owning SysML thread
The contract is useful only if it parses, attaches correctly, generates compatible code, and discharges downstream proofs.
Source: Tahat et al., DASC 2026, Listing 1 and Sec. II-A.
9
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:10
Presenter focus: explain GUMBO enough for nonexperts without losing FM experts.
What I would say:
GUMBO is the behavioral contract layer attached to the SysML v2 architecture. In this example, natural language such as “if the regulator is in normal mode and the temperature is below the lower bound, heat control shall be on” becomes assumptions, guarantees, and compute cases. The important point is that a GUMBO contract is not just text. It must be attached to the correct architectural element, translated through HAMR, and discharged by Logika. Requirements that imply memory—such as hysteresis or “hold previous”—need explicit state and initialization. That was a key failure mode for the baseline.
Presenter suggestion: do not walk through every line of code; explain the blocks: state, initialize, compute, compute cases.
Claim guardrail: this is illustrative; the evaluation contains many target units.
Transition: The next slide shows how a Meta-Rule captures this decision pattern.
<number>

## Slide 10
Method: Meta-Rules store reusable decisions
A rule links trigger, formal choice, structural placement, and verifier-gated repair.
Trigger
What wording or diagnostic activates the rule?
Semantic choice
Which formal construct captures the intent?
Structural placement
Where must it live in SysML v2 / GUMBO?
Repair gate
Which diagnostics drive the smallest safe repair?
Example A - memory / hysteresis rule
Trigger: “hysteresis”, “hold previous”, “shall not change”
Choice: model memory as explicit state + initialization
Placement: attach compute_cases to the behavior-owning thread
Gate: retain only if HAMR / Slang / Logika checks succeed
Example B - architecture / attachment rule
Trigger: requirement constrains a component; “receives / sends / flows to”
Choice: map interfaces to typed ports and data-flow endpoints
Placement: attach GUMBO to the project-owned behavior thread
Gate: preserve generated Slang names; repair from HAMR diagnostics
Stored as local, version-controlled rule books: inspectable • reviewable • replayable • rollback-capable.
Sources: Tahat et al., DASC 2026, Listing 2; Combined Process Meta-Rule Book, MR-PORT-001 and MR-GUMBO-ATTACH-001.
10
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:10
Presenter focus: define exactly what is stored in a Meta-Rule.
What I would say:
A Meta-Rule is not just a better prompt. It has a reusable structure. It records the linguistic or diagnostic trigger, the semantic formalization choice, the structural placement in SysML v2 or GUMBO, and the repair or acceptance gate. For the memory example, the trigger is words like hysteresis or hold previous. The semantic choice is explicit state and initialization. The structural placement is the behavior-owning thread. The repair gate is HAMR/Slang/Logika success. This turns a transient interaction into a governed artifact that can be reviewed, version controlled, replayed, or rolled back.
Presenter suggestion: point to the four boxes in order and repeat “trigger, choice, placement, gate.”
Claim guardrail: the model is still stochastic; the retained rule is what becomes governed.
Transition: The algorithm has two modes: learn the rule book, then apply it.
<number>

## Slide 11
Method: Developer mode learns; user mode applies
Developer mode creates governed rule memory; user mode applies the frozen library under the same gates.
Developer mode - supervised self-adaptation
1
Start from golden requirement + verified contract
2
EXTRACTRULE proposes a candidate Meta-Rule
3
APPLYRULE tests a sampled subset
4
Tune ε; verify / repair within budget B
5
Retain only if success ≥ τ and human approves
User mode - rule-guided application
1
Load frozen, curated Meta-Rule library
2
Synthesize candidate contracts from new requirements
3
Run HAMR / Logika integration and code checks
4
Repair the smallest failing fragment while B remains
5
Store verified artifacts and traces; flag unresolved failures
Golden pair G
EXTRACTRULE
sample + d ≤ ε
V(ĝ, B)
human gate
retain M / apply
B = time + token + repair-cycle budget | ε = reuse-scope threshold | τ = minimum acceptance threshold
Source: Tahat et al., DASC 2026, Sec. III-B, Algorithm 1, and Listing 3.
11
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:10
Presenter focus: separate developer-mode investment from user-mode reuse.
What I would say:
Developer mode is where the rule book is learned and governed. Starting from golden requirement–contract pairs, EXTRACTRULE proposes a candidate Meta-Rule, APPLYRULE tests it on a sample, the verifier checks candidates within budget, and a human approves before retention. User mode is different: the curated library is frozen and applied to the target requirements. This separation matters for measurement. The accepted paper reports a conservative adjusted trace that includes the one-time extraction and refinement effort; later user-mode reuse is faster once the rule book exists.
Presenter suggestion: say “learn once, apply repeatedly—but still verify every time.”
Claim guardrail: human review remains part of the retention process.
Transition: The first hero animation explains how far a learned rule is allowed to generalize.
<number>

## Slide 12
Method: How far can a rule generalize?
Similarity screens candidate reuse; verification, budget, and human review decide retention.
Source: Tahat et al., DASC 2026, Fig. 2; animation uses original paper figure as the base.
Generalize only as far as proof and budget allow.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:45
Presenter focus: Similarity screens candidate reuse; verification, budget, and human review decide retention.
What I would say:
This is the central geometric intuition. The verified golden example gives a direction, not a guarantee. A candidate rule is worth trying only when the new requirement is close enough under the reuse-scope threshold. But similarity is only a screen. HAMR/Logika verification, the time-token repair budget, and human review decide whether the rule becomes retained engineering memory.
Presenter suggestion: play the animation only once and then pause briefly on the final frame.
Claim guardrail: the figure is a paper-grounded conceptual aid; correctness is decided only by the external verification workflow and the stated experimental scope.
Transition: Continue to the next slide by connecting the visual mechanism to the benchmark and results.

## Slide 13
Method: How SCP reaches proof
Meta-Rules guide generation; diagnostics drive repair; proofs are the acceptance gate.
Source: Tahat et al., DASC 2026, Fig. 1; animation uses original paper workflow as the base.
Accepted evidence emerges from the loop, not fluent text alone.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:45
Presenter focus: Meta-Rules guide generation; diagnostics drive bounded repair; proof artifacts are the acceptance gate.
What I would say:
This is the main system story. English requirements and architecture context enter the specification agent. Meta-Rules narrow the proposal before expensive downstream checks. HAMR and Logika then act as hard gates. Successful checks emit proof artifacts; failures return diagnostics to the repair agent. The loop is bounded by time, tokens, and repair cycles.
Presenter suggestion: play the animation only once and then pause briefly on the final frame.
Claim guardrail: the figure is a paper-grounded conceptual aid; correctness is decided only by the external verification workflow and the stated experimental scope.
Transition: Continue to the next slide by connecting the visual mechanism to the benchmark and results.

## Slide 14
Evidence: The incumbent Isolette system
A realistic infant-incubator benchmark spanning requirements, SysML v2, generated code, and proof.
Sources: Lempia & Miller, FAA REMH (2009); Tahat et al., DASC 2026, Sec. V-A; Hatcliff et al., Isolette system.
14
Inputs
FAA Requirements
Engineering Management
Handbook
text • tables • figures • cross-references
Existing SysML v2
models + shared libraries
Monitor.sysml • Regulate.sysml
Realistic friction: hysteresis, “no change,” naming, attachment, and cross-file dependencies.
Incumbent system
Monitor
temperature status
alarm status
Regulate
heat-control
commands
Sensors / operator
inputs and modes
Actuators / displays
heater and alarms
One formalization choice must survive model placement, code generation, and proof discharge.
Defined evaluation
scope
42
proof-bearing
units
Monitor + Regulate
• GUMBO contract-bearing blocks
• generated / modified compute_cases
• HAMR-generated methods checked by Logika
Train: small solved file/subsystem
Evaluate: remaining target files
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:20
Presenter focus: establish the benchmark as an incumbent system-level case.
What I would say:
This is not a toy text-to-contract prompt. Isolette is an incumbent infant-incubator benchmark with Monitor and Regulate subsystems, sensor and operator inputs, and actuator outputs. The inputs include realistic FAA-style material plus existing SysML v2 models and shared libraries. Our quantitative scope is explicitly 42 proof-bearing units across Monitor and Regulate. The key challenge is that one formalization decision must survive model placement, HAMR generation, generated Slang/Scala obligations, and Logika proof discharge.
Suggestion to presenter: point to the center flow first, then the 42-unit scope; do not begin with the dense input list.
Transition: now show why the prompt-only baseline failed on a concrete memory requirement.
<number>

## Slide 15
Evidence: Why the prompt-only run failed
After 33 minutes and 19.74M context tokens, unsupported memory idioms still blocked verification.
Source: Tahat et al., DASC 2026, Listing 4 and Table II; condensed listing reproduced for readability.
15
Observed prompt-only failure (paper Listing 4)
Parser rejected memory idioms:
"rejects every variant of the state ... syntax"
"@pre as an unsupported classification test"
Result: could not encode hysteresis / no-change cases.
Tokens: input=981,770 (+18,673,920 cached), output=85,833.
Why the run stalled
• The toolchain-specific state pattern was absent from the transient context.
• Parser failures prevented downstream implementation and proof obligations from converging.
• After substantial context use, the agent asked for an example instead of producing a verified artifact.
33 min
wall-clock time
19.74M
context tokens
2 / 42
verified units
0
end-to-end success
Long context did not recover the niche, tool-accepted memory pattern.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:15
Presenter focus: make the failure mode readable without relying on a screenshot.
What I would say:
The baseline did not simply make one typo. It repeatedly tried pre-state idioms that the SysML v2 GUMBO toolchain did not accept. The paper records the key messages: every state-syntax variant was rejected, @pre was interpreted as unsupported, and the run could not encode hysteresis or no-change cases. After 33 minutes and 19.74 million context tokens, only 2 of 42 units verified and the end-to-end result was still zero.
Suggestion to presenter: read only the two quoted lines, then immediately point to 2 of 42.
Transition: the next slide shows the reusable decision pattern that changed the search policy.
<number>

## Slide 16
Evidence: What Meta-Rules changed
Explicit state, initialization, correct placement, and verifier-guided repair completed the proof path.
Sources: Tahat et al., DASC 2026, Listing 1, Sec. V-B-C, and Table II. Code block is a representative accepted pattern.
16
Reusable decision pattern
1
Memory language
hysteresis / hold previous → explicit state
2
Initialization
constrain the previous command at startup
3
Structural placement
attach compute_cases to the behavior-owning thread
4
Repair gate
change only the smallest fragment indicated by HAMR / Logika
Representative accepted GUMBO pattern
state lastCmd: On_Off;
initialize
guarantee initLastCmd:
lastCmd == Off;
compute_cases
case REQ_2:
assume mode == NORMAL
&& temp < lower;
guarantee heat_control ==
On;
39 min
complete adjusted run
13.83M
context tokens
42 / 42
verified units
1
end-to-end success
The conservative complete adjusted trace already includes the one-time rule extraction and refinement effort.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:20
Presenter focus: explain what changed, not merely that the run succeeded.
What I would say:
The learned Meta-Rule changed the search policy. Memory-bearing language now triggers explicit state and initialization. The contract is placed on the behavior-owning thread, and HAMR or Logika diagnostics drive only the smallest safe repair. The center code is a representative accepted pattern from the paper: state, initialization, and compute cases. With this policy, the complete adjusted run verified all 42 units. Importantly, the 39-minute and $0.92 results later in the talk already include the one-time extraction and refinement effort.
Suggestion to presenter: trace the four decisions on the left, then point to 42 of 42; do not read the code line by line.
Transition: now define the metrics used to compare the two runs fairly.
<number>

## Slide 17
Metrics: Verified outcomes, not tokens alone
The metrics normalize by accepted proof-bearing units.
ρ
Verification coverage
|Uverified| / |U|
fraction of targeted proof-bearing units discharged
Θ
Verified throughput
|Uverified| / Twall
verified units per minute
K
Context tokens / verified unit
Nctx / |Uverified|
input + cached input + output per accepted unit
K$
Dollar cost / verified unit
C / |Uverified|
illustrative provider pricing normalized by success
S
End-to-end success
1 iff ρ = 1 and checks complete
integration- and code-level target scope completed
Token classes remain visible: uncached input, cached input, and output-side tokens. Dollar values are illustrative; the reproducible evidence is the logged token accounting.
Source: Tahat et al., DASC 2026, Sec. V-C, Eqs. (1)-(8), Table II.
17
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:55
Presenter focus: prepare the audience to value cost per verified unit.
What I would say:
We measure verified outcomes, not token counts in isolation. Coverage is the fraction of targeted proof-bearing units discharged. Throughput is verified units per minute. Context tokens per verified unit accounts for the cost of reaching accepted artifacts. Dollar cost per verified unit is illustrative and pricing-model dependent, so the stable evidence is the token-class accounting. End-to-end success means the scoped target is fully verified. These metrics prevent an optimization that simply verifies less or hides failures.
Presenter suggestion: keep this slide brisk. It exists to make the next two result slides credible.
Claim guardrail: dollar values are illustrative; token classes and verification outcomes are the core measured quantities.
Transition: The first result is verification coverage and throughput.
<number>

## Slide 18
Results: 2 of 42 becomes 42 of 42
Orange = prompt-only baseline • blue = complete adjusted run • gray = later reuse after the book exists.
Verification coverage ρ
0
25
50
75
100
4.76%
No rules
100%
Adjusted FSE
2 / 42 → 42 / 42 verified target units
Verified throughput Θ (units/min)
0.0
0.5
1.0
1.5
2.0
0.06
Baseline
1.08
Adjusted
1.68
Later reuse
18× adjusted gain; reuse is faster after the book exists
Source: Tahat et al., DASC 2026, Table II and Fig. 3. Adjusted throughput includes the one-time rule-book effort.
18
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:05
Presenter focus: tell the main quantitative story.
What I would say:
Here is the main accepted-paper result. The prompt-only baseline verified 2 of 42 units, or 4.76 percent coverage. The adjusted Meta-Rule-guided run verified all 42, reaching 100 percent coverage in the defined target scope. Throughput also changed: from 0.06 units per minute to 1.08 units per minute in the conservative complete adjusted run, which includes the one-time learning effort. The gray bar is the later user-mode reuse reference after the rule book exists, at 1.68 units per minute.
Presenter suggestion: speak the color legend: orange is baseline, blue is adjusted complete, gray is later reuse.
Claim guardrail: distinguish the 1.08 conservative result from later reuse.
Transition: The second result is the effective cost of verified evidence.
<number>

## Slide 19
Results: Cost per verified unit drops ~30x
The denominator changes from two verified units to forty-two.
Context tokens per verified unit K
log-scaled bar length
Baseline
9.87M
Adjusted
329K
Later reuse
111K
≈30× lower adjusted context per verified unit
Illustrative dollar cost per verified unit
Baseline
$41.04
Adjusted
$0.92
Later reuse
$0.79
Adjusted cost includes one-time extraction / refinement
Pricing is illustrative; token classes and verified-unit normalization are the reproducible evidence.
Source: Tahat et al., DASC 2026, Table II and Fig. 3. Pricing reference: OpenAI API pricing page cited in the paper.
19
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:05
Presenter focus: explain why cost per verified unit is the right economic measure.
What I would say:
The cost result is not only that the adjusted run used fewer tokens. The denominator changed from 2 verified units to 42 verified units. Context tokens per verified unit fell from about 9.87 million to about 329 thousand in the conservative adjusted trace. The illustrative dollar cost per verified unit fell from $41.04 to $0.92. The later reuse trace is shown separately at about 111 thousand context tokens per verified unit and $0.79. This is the practical value of reusable rule memory: fewer failed branches, fewer repeated logs, and more accepted proof artifacts per unit of context.
Presenter suggestion: say “cost of accepted evidence,” not simply “cost of generation.”
Claim guardrail: prices change; present dollars as illustrative and token classes as reproducible.
Transition: This puts Meta-Rules in the gap between fine-tuning and prompt-only ICL.
<number>

## Slide 20
Value: Specialization without fine-tuning
A governed specialization asset when fine-tuning is restricted.
 | Fine-tuning | Prompting / ICL | Meta-Rules
Persistent across runs | Yes | No | Yes (external)
Model weights tuning | Explicit | Implicit | Implicit
Cost | High | Med | Low-Med
Auditability / review | Low | Low-Med | High
Governance / rollback | Low | Low | High
Runtime context overhead | Low | High | Low-Med
Data / IP constraints | High | Low-Med | Low
FV acceptance gates | N/A | N/A | Primary
HAMR toolchain reuse | N/A | Ad hoc | Primary
When weight tuning is restricted, Meta-Rules provide a governed specialization asset rather than transient prompt behavior.
Source: Tahat et al., DASC 2026, Table I and Sec. IV-D.
20
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:00
Presenter focus: connect method to the restricted-fine-tuning challenge.
What I would say:
This table explains why Meta-Rules are the right adaptation mechanism for this setting. Fine-tuning can be powerful, but it requires data, authorization, compute, and checkpoint governance that may be difficult in aerospace settings. Prompt-only ICL avoids weight updates, but the behavior is transient and context-heavy. Meta-Rules occupy the middle: they preserve task specialization externally, without changing model weights, while keeping auditability, rollback, and formal-verification acceptance gates. This is an operational surrogate for fine-tuning, not a universal substitute for all domains.
Presenter suggestion: do not read the table. Highlight three rows: persistence, auditability, and FV acceptance gates.
Claim guardrail: say “operational surrogate,” not “equivalent to fine-tuning.”
Transition: Next, position the work relative to related systems.
<number>

## Slide 21
Related work: Where SCP differs
This non-comprehensive comparison describes publicly demonstrated scope—not overall product or research quality.
Category / examples
NL → formal spec
MBSE / stack aware
Generated implementation
Formal checker / proof
Open artifacts
Theorem proving / proof repair [19–21]
GPT-f, Baldur, CoqDog
◐
–
–
✓
◐
Model / code verification [22–24, 27]
F*, automated reasoning, VeriStruct
◐
◐
◐
✓
◐
MBSE / model-level tools [22–23]
Imandra SysML, AGREE-Dog
◐
✓
◐
◐
◐
Commercial assistants [23–26]
Kiro, ImandraX, Aristotle, Axiom / AXLE
✓
◐
◐
◐
◐
SCP Meta-Rules [1, 14]
INSPECTA: SysML v2 + GUMBO + HAMR + Logika
✓
✓
✓
✓
✓
✓
demonstrated in cited scope
◐
partial / varied public scope
–
not the stated scope
SCP: natural language → architecture → formal contracts → generated implementation → proof
Sources: DASC 2026 Sec. VI and references [19–27]; public product pages for Kiro, ImandraX, Aristotle, and Axiom/AXLE. Scope comparison, not ranking.
21
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:55
Presenter focus: differentiate without overstating.
What I would say:
The related-work point is not that other systems are unimportant. The point is boundary and artifact. Theorem-proving and proof-repair systems focus on proof scripts or theorem libraries. Model-level MBSE tools can reason about architecture models. Commercial specification-driven tools structure AI development around requirements. SCP differs by connecting natural-language requirements to SysML v2/GUMBO contracts, HAMR-generated implementation artifacts, and Logika proof discharge in one toolchain-aware loop. The learned artifact is also different: an auditable, reusable, verifier-gated rule layer.
Presenter suggestion: explicitly say “scope comparison, not a ranking.”
Claim guardrail: do not imply every commercial tool lacks verification; describe the specific evaluated boundary of SCP.
Transition: The next slide is deliberately honest about limitations and next acceptance gates.
<number>

## Slide 22
Next: Scope, limits, and extension
Strong evidence is more persuasive when claim boundaries are explicit.
Accepted paper establishes
Isolette / HAMR / INSPECTA scope
GUMBO-centered formalization + repair
42 proof-bearing units; JVM / Slang path
Cross-file and cross-subsystem reuse - not universal generality
Post-paper “so far” milestone
KSU HAMR docs + Claude-oriented training + Collins repair experience distilled into 10 auditable Meta-rules books
Process, thread, port, connection, scheduling, GUMBO, Slang, seL4, traceability, repair
100+ HAMR-scoped proof-bearing units.
Next acceptance gates
New Open Platform examples as heterogeneous held-out systems
Automatic structural equivalence to golden systems
System-wide naming + contract completeness + score calibration
Rust / Verus, seL4 / Microkit, and approved small / local models
Broader reuse is being tested - not assumed. The next milestone is heterogeneous-system transfer with automatic structural validation.
22
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 1:05
Presenter focus: show maturity by bounding the claim and naming next tests.
What I would say:
The accepted result is strong, but scoped. It establishes GUMBO-centered formalization and repair in the Isolette/HAMR/INSPECTA workflow, using the JVM/Slang path. It is not a universal cross-system generalization claim. The ongoing extension is promising: ten HAMR-scoped rules now cover process, thread, port, connection, scheduling, GUMBO attachment, Slang compatibility, traceability, seL4/Microkit mapping, and verifier repair. The next acceptance gate is broader validation: newest KSU examples as held-out systems, automatic structural-equivalence checks against golden systems, and careful separation of rule extraction, orchestration, application, verification, time, and token costs.
Presenter suggestion: reviewers trust results more when limitations are stated cleanly.
Claim guardrail: label the ten-rule combined book as post-paper ongoing work.
Transition: Close with the three claims the audience should remember.
<number>

## Slide 23
Close: Three takeaways
The result is open, measured, and verifier-gated.
1
The problem is verified engineering, not plausible generation.
SCP begins from natural-language requirements, but external formal tools and human review decide acceptance.
2
The intellectual nugget is persistent verifier-gated specialization.
Meta-Rules crystallize successful in-context behavior into governed, reusable compact rule memory within the INSPECTA/HAMR toolchain.
3
The scoped evidence is strong and measurable.
42 / 42 verified units, 18× adjusted throughput, and about 30× lower context cost per verified unit.
Open artifacts
loonwerks/INSPECTA-Spec-Code-Proof-Copilot
Verified demo
Meta-Rule-guided successful run
Baseline demo
Prompt-only failure trace
Thank you. Questions?
23
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: 0:45 + Q&A
Presenter focus: close with the paper’s strongest scoped claims.
What I would say:
The problem is verified engineering, not plausible generation. The intellectual nugget is persistent, verifier-gated specialization without weight updates. The scoped evidence is strong: the Meta-Rule-guided run reaches 42 of 42 proof-bearing units with an 18x adjusted throughput gain in the accepted-paper scope. The repository contains the rule books, plans, evaluation artifacts, and demos. I am happy to take questions.
<number>

## Slide 24
References: Paper, toolchain, and benchmark
[1] Tahat et al., “Bridging Natural Language to Verified Implementation: A Neuro-Symbolic High-Assurance MBSE Pipeline in SysML v2,” IEEE/AIAA DASC 2026.
[2] Hardin et al., “Automated SysML v2 System Model to Memory-Safe Language Code Generation for Avionics Applications,” DASC 2025.
[3] Lempia and Miller, Requirements Engineering Management Handbook, FAA, DOT/FAA/AR-08/32, 2009.
[4] Hatcliff et al., “The Isolette System: Illustrating End-to-End Artifacts for Rigorous Model-Based Engineering,” ISoLA 2024.
[5] OMG, SysML v2 Specification, 2025.
[6] Hatcliff et al., “An AADL Contract Language Supporting Integrated Model- and Code-Level Verification,” Ada Letters, 2023.
[7] Galois, GUMBO: Grand Unified Modeling of Behavioral Operators, 2024.
[8] Hatcliff et al., “HAMR: An AADL Multi-Platform Code Generation Toolset,” ISoLA 2021.
[9] Sireum HAMR, Kansas State University, 2025.
[10] de Moura and Bjørner, “Z3: An Efficient SMT Solver,” TACAS 2008.
[11] Barrett et al., “CVC4,” CAV 2011.
[12] Belt et al., “Model-Driven Development for the seL4 Microkernel Using HAMR,” Journal of Systems Architecture, 2023.
[13] Klein et al., “seL4: Formal Verification of an OS Kernel,” SOSP 2009.
[14] Loonwerks, INSPECTA Spec-Code-Proof Copilot repository, 2026: github.com/loonwerks/INSPECTA-Spec-Code-Proof-Copilot.
24
Selected references used in the talk.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: backup / do not present unless asked
Presenter focus: references for paper, benchmark, and toolchain.
What I would say if this slide appears:
These are the primary sources for the paper, toolchain, benchmark, and artifacts. The most important references for the main talk are the DASC 2026 paper, HAMR/INSPECTA work, the FAA Requirements Engineering Management Handbook source material, the Isolette benchmark, SysML v2, GUMBO, HAMR, Logika, and the open-source repository.
Presenter suggestion: keep reference slides after thank-you so they do not interrupt the story.
Claim guardrail: use this slide to answer source questions, not as part of the main timed talk.
Transition: If a question is about learning foundations or related systems, move to the next reference slide.
<number>

## Slide 25
References: Learning foundations and related systems
[15] von Oswald et al., “Transformers Learn In-Context by Gradient Descent,” ICML 2023.
[16] Achille and Soatto, “AI Agents as Universal Task Solvers,” Entropy 28(3), 2026.
[17] Gurnee et al., “Verbalizable Representations Form a Global Workspace in Language Models,” arXiv:2607.15495 / Anthropic Transformer Circuits, 2026.
[18] Launchbury, “A DARPA Perspective on Artificial Intelligence,” DARPA TV, 2017.
[19] Polu and Sutskever, “Generative Language Modeling for Automated Theorem Proving,” 2020.
[20] First et al., “Baldur: Whole-Proof Generation and Repair with Large Language Models,” 2023.
[21] Tahat et al., “Proof Repair Utilizing Large Language Models: A Case Study on the Copland Remote Attestation Proofbase,” AISoLA 2024.
[22] Tahat et al., “AGREE-Dog Copilot: A Neuro-Symbolic Approach to Enhanced MBSE,” AISoLA 2025.
[23] Imandra, Imandra SysML / ImandraX public product pages, accessed 2026.
[24] Kiro, spec-driven development and property-based testing public product pages, accessed 2026.
[25] Harmonic, “Aristotle: IMO-Level Automated Theorem Proving,” 2025/2026.
[26] Axiom Math, AXLE - Axiom Lean Engine public documentation, accessed 2026.
[27] Sun et al., “VeriStruct: AI-Assisted Automated Verification of Data-Structure Modules in Verus,” 2025.
[28] OpenAI API pricing documentation, accessed 2026. Prices and thresholds are time-dependent.
25
Selected references used in the talk.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: backup / do not present unless asked
Presenter focus: references for learning foundations and related systems.
What I would say if this slide appears:
These references support the framing around in-context learning, task-solving transfer, contextual adaptation, and related proof/verification systems. For the talk, I use the Anthropic workspace idea only as a motivating analogy for compact abstraction, not as a mechanistic claim about our Meta-Rules.
Presenter suggestion: be ready to distinguish motivation from evidence.
Claim guardrail: do not cite these works as proving SCP; the SCP evidence comes from the Isolette/HAMR experiment.
Transition: For detailed numeric questions, use the metric backup slide.
<number>

## Slide 26
Backup: Complete accepted-paper metrics
Metric | Baseline: no Meta-Rules | Adjusted ε = 0.1: GUMBO FSE book
Twall (min) | 33 | 39
Nin | 981,770 | 381,624
Ncache | 18,673,920 | 13,391,360
Nout | 85,833 | 57,821
Nin + Nout | 1,067,603 | 439,445
Illustrative run cost | $82.08 | $38.51
Nctx | 19,741,523 | 13,830,805
Context burn rate | ≈598K/min | ≈355K/min
Targeted units | 42 | 42
Verified units | 2 | 42
Coverage ρ | 4.76% | 100%
Throughput Θ | 0.06 units/min | 1.08 units/min
Context / verified unit | ≈9.87M | ≈329K
Dollar / verified unit | $41.04 | $0.92
End-to-end success S | 0 | 1
Source: Tahat et al., DASC 2026, Table II.
26
Source: DASC 2026 paper, Table II.
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: backup / numeric detail
Presenter focus: provide the complete accepted-paper table if someone asks about accounting.
What I would say if this slide appears:
This backup slide contains the full accepted-paper metric table. The important accounting point is that the adjusted column is a complete logged run: it already includes the one-time extraction and refinement effort plus the successful verification run. The cached tokens affect context size and burn rate, but the illustrative dollar calculation uses the pricing model stated in the paper.
Presenter suggestion: use this only for technical Q&A; do not walk through every row during the main talk.
Claim guardrail: prices are not invariant; token classes and verification counts are the stable evidence.
Transition: For post-paper rule-book questions, use the ten-rule backup.
<number>

## Slide 27
Backup: Ten retained HAMR Meta-Rules
Post-paper extension; not part of the accepted paper’s 42-unit quantitative claim.
Rule ID | Reusable purpose | Domain | Confidence
MR-PROC-001 | Process definitions from subsystem / deployment text | HAMR | 0.88
MR-THREAD-001 | Behavioral thread inside each project-owned process | HAMR | 0.90
MR-SEL4-PROC-001 | One thread per process for seL4 / Microkit targets | seL4 | 0.84
MR-PORT-001 | English interface verbs to typed ports | SysML v2 | 0.89
MR-CONN-001 | Data-flow phrases to connection endpoints | SysML v2 | 0.82
MR-SCHED-001 | Timing / deployment phrases to scheduling and binding | AADL map | 0.78
MR-GUMBO-ATTACH-001 | Attach GUMBO to behavior-owning thread | GUMBO | 0.92
MR-TRACE-001 | Preserve traceability from English sources | Traceability | 0.86
MR-SLANG-COMPAT-001 | Preserve downstream Slang component compatibility | Slang | 0.80
MR-VERIFY-PROC-001 | Treat HAMR / Logika diagnostics as repair signals | Verification | 0.83
Source: Combined Process Meta-Rule Book; extended SCP manuscript, combined HAMR-scoped rule table.
27
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: backup / ongoing work detail
Presenter focus: show what is in the combined HAMR rule book without expanding the accepted claim.
What I would say if this slide appears:
This is the post-paper combined HAMR rule book. The ten retained rules cover process definitions, behavioral threads, seL4/Microkit process mapping, ports, connections, scheduling and binding, GUMBO attachment, traceability, downstream Slang compatibility, and verifier-guided repair. This is promising HAMR-scoped evidence and a clear next direction, but it is not part of the accepted paper’s 42-unit quantitative claim.
Presenter suggestion: say “ongoing extension” before describing the table.
Claim guardrail: broader heterogeneous-system validation remains next work.
Transition: For questions about cost or reproducibility, use the measurement backup.
<number>

## Slide 28
Backup: Measurement and pricing plan
Separate developer-mode investment from user-mode reuse and report every stage in time and token terms.
Developer mode
1
rule extraction
2
sample calibration
3
human review
4
verification / repair
User workflow
1
human request / approval
2
orchestration
3
rule application
4
verification / repair
Reported measures
1
wall-clock time
2
uncached / cached input
3
output / reasoning
4
repair count + verified units
Pricing note: the paper reports token classes and a symbolic pricing model because provider prices and thresholds change. Input, cached input, and output are kept distinct.
Sources: Tahat et al., DASC 2026, Sec. V-C; OpenAI API pricing documentation.
28
© 2026 Collins Aerospace. | Collins Aerospace Property | This document does not include any export controlled technical data.
Notes: Timing: backup / measurement plan
Presenter focus: explain how future reports will separate learning investment from user workflow.
What I would say if this slide appears:
The measurement plan separates developer-mode training from user-mode application. Developer mode includes rule extraction, sample calibration, and human review. User workflow includes orchestration, rule application, verification, repair, and final artifact storage. For each stage, we should report wall-clock time, input/cached/output/reasoning tokens where available, repair count, and whether the verification target was reached. This prevents cost claims from mixing one-time investment with later reuse.
Presenter suggestion: use this slide to answer fairness or reproducibility questions.
Claim guardrail: future cost reductions should be reported with token classes, not only dollar values.
Transition: Return to the closing slide or Q&A.
<number>